## Slide 1: Power Electronics For The Geec
Conor Farrell 2025-2026
MECE - 21359763

## Slide 2: Project Overview
The GEEC (Galway Energy Efficient Car) is a participant in the Shell Eco Marathon.
It’s entered in the prototype lithium-ion class.
The highest score GEEC achieved was 354km/kWh or 23c to drive from here to Dublin.
Power Electronics Requirements:
Drive an Electric Motor.
Take Throttle input from the driver
Fail Safe
Notes: BG
GEEC – SEM prototype lithium ion
DAQ – voltage current power speed temp gps
Driver display
Benefit to mechanicals

## Slide 3: Current Power Electronics
Inflexible
Obsolete Components
2 Layer Design
Large Loop Area, resulting in LC resonator
Field Modifications

## Slide 4: The Project Scope
Semester 1: Power Electronics
4 layer SMD
Full isolation
Semester 2:
Power Controller
2 layer THT
Closed Loop Feedback

## Slide 5: Brushless Motors
Previous Projects Investigated Brushless Controllers & 48V control
Theoretical Calculations show worse performance ~2%
Chart: Motor Efficiency vs Duty Cycle

## Slide 6: Current Control
Hardware Limiting:
  Cycle-by-Cycle (10-30kHz)
  Latching
Software Control:
  ~10Hz
  PID loop

## Slide 7: Simulation
Closed Loop Current Control
Variable Current Limit

## Slide 8: Testing
Orange: AD8411A
Green: ADuM3190 Expected AV: 1 Actual AV: 0.33
Solution: Op-Amp (AV 2) and 800kHz low pass filter on Power Controller.

## Slide 9: Protection
Low power digital and analogue isolators.
  Consumes 46mW
TVS Diodes to shunt 15A at 38V

## Slide 10: Schematic
Half Bridge Design
  40 10µF MLCC Capacitors & 3 4.7mF Electrolytic Capacitors
  Redundant MOSFETS for easy Replacement
  TVS Diodes Capable of shunting 15A @ 38V
  Indicator LED with removable jumper.

## Slide 11: PCB Design
4 Layer Board, Isolated Ground planes
Via Stitching on High current planes
Minimisation of loop area and change in loop area
Preliminary Design

## Slide 12: This Semester
Design Power Controller Board
Assist in Design of DAQ Board
Testing of Hardware
Implement Control System
Integrate the Design into the DAQ
Determine Performance Improvement

## Slide 13: Thanks For Listening
Any Questions?